Family History Library

Purchase Microfilm Quality Standard

21 November 1994

|  | Standards for Original Camera Negative | Standards for Film Duplicates (negative & Positive) |
| --- | --- | --- |
| Quality Check Points | (class I inspection) | (class II inspection) |
|  | Quality is Ideal If: | Quality is Acceptable If: |
| Group 1/Good Contrast |  |  |
| Density Variation | .30 or less | .40 or less |
| Background Density | .80-1.30 | .70-1.40 |
|  |  | (negative only) |
| Group 2/Medium Contrast |  |  |
| Density Variation | .25 or less | .35 or less |
| Background Density | .80-1.20 | .70-1.30 |
|  |  | (negative only) |
| Group 3/Poor Contrast |  |  |
| Density Variation | .20 or less | .30 or less |
| Background Density | .80-1.10 | .70-1.30 |
|  |  | (negative only) |
| Base plus fog density | .10 or less | .20 or less |
| Resolution | 2mm character height 4.5 pattern minimum | 2mm character height 4.0 pattern minimum |
| and | and | and |
| Image Quality | Readable at a glance through four generations | Readable through three generations |
| Missing or covered information | all information present and readable | All significant information present and readable |